## Slide 1: I: BASIC CONCEPTS
By – Dr. S. C. Dharmadhikari

## Slide 2: Agenda
Part I | Introduction to Computer Graphics, Basics of graphics systems, Raster scan & Random scan displays, basic display processor
Part II | Display Files: display file structure, algorithms and display file interpreter. Primitive operations on display file
Part III | Plotting Primitives: Scan conversions, lines, line segments, vectors, pixels and frame buffers, vector generation
Part IV | Line drawing Algorithms: DDA, Bresenham Circle drawing Algorithms: - DDA, Bresenham
Part V | Character Generation: Stroke Principle, Starburst Principle, Bit map method, Introduction to aliasing and anti-aliasing

## Slide 3: Part I : Graphics Primitives.
Computer Graphics : It deals with pictures and images.
It makes a computer capable of displaying and manipulating pictures.
For example, laser printers , plotters, monitor .

## Slide 4: Architecture Of A Graphics System
System Bus
CPU
Display Processor
System Memory
Display Processor Memory
Frame Buffer
Video Controller
Monitor
Monitor

## Slide 5
Refreshing :
D.A. circuitry repeatedly reads information from DP memory and transfers it onto screen so as to make the image displayed on screen steadily and clearly.
[ 50 to 70 times a second ]
Refresh Rate
Low refresh rate causes flickering.

## Slide 6: Types Of D.A.
  Monochrome Adapter [ MA ]
  Hercules Adapter [ HA ]
  Color Graphics Adapter [ CGA ]
  Enhanced Graphics [ EGA ]
  Multicolor Graphics Adapter [ MCGA ]
  Video Graphics Adapter [ VGA ]
  Super Video Graphics Array [SVGA ]
  Extended Graphics Adapter [XGA ]

## Slide 7: Different Modes
1> Character mode
Programs running in character mode are severely limited.
In character mode, the display screen is treated as an array of blocks, each of which can hold one ASCII character.
2> Graphics mode.
Programs that run in graphics mode can display an unlimited variety of shapes and fonts
In graphics mode, the display screen is treated as an array of pixels. Characters and other shapes are formed by turning on combinations of pixels.

## Slide 8: Graphics Primitives
Pixel : Picture Element, a pixel is a single point in a graphic image.
Arranged in rows and columns. The pixels are so close together that they appear connected.
The number of bits used to represent each pixel determines how many colors or shades can be displayed.
Resolution : The quality of a display system largely depends on its resolution i.e. how many pixels it can display. It refers to the sharpness and clarity of an image.
For example, a 640-by-480 pixel screen is capable of displaying 640 distinct dots on each of 480 lines, or about 300,000 pixels.

## Slide 9: Types
There are two kinds of displays–
1) raster (composed of pixels) and
2) vector (composed of paths).

## Slide 10: RASTER GRAPHICS
On a computer monitor, images are nothing more than variously colored pixels. Certain kinds of image-file formats record images literally in terms of the pixels to display.
Raster images are more commonly called bitmap images.
A bitmap image uses a grid of individual pixels where each pixel can be a different color or shade. Bitmaps are composed of pixels.
A bitmap become jagged as it is scaled up.
The jagged appearance of bitmap images can be partially overcome with the use of "anti-aliasing".

## Slide 11
Raster( Bitmap ) Image | Vector Image

## Slide 12: Raster Scan Systems
Draw one line at a time

## Slide 13
Anti-aliasing is the application of subtle transitions in the pixels along the edges of images to minimize the jagged effect.
One can edit the image only by altering the pixels directly with a bitmap editor.
Photoshop and Paint Shop Pro are two of the most popular bitmap editors.

## Slide 14: VECTOR GRAPHICS ( Random Scan )
Vector image files record images descriptively, in terms of geometric shapes. These shapes are converted to bitmaps for display on the monitor.
Vector graphics use mathematical relationships between points and the paths connecting them to describe an image. Vector graphics are composed of paths.
Vector images are easier to modify, because the components can be moved, resized, rotated, or deleted independently.
PostScript is a popular vector format for printing, but so far Macromedia's Flash is the closest thing to a standard vector format on the Web.

## Slide 15
Designed for line-drawing applications, such as architectural and engineering layouts, and they cannot display realistic shaded scenes.
Refresh rate on a random-scan system depends on the number of lines to be displayed on that system. Picture definition is now stored as a set of line-drawing commands in an area of memory referred to as the display list, refresh display file, vector file, or display program.
To display a specified picture, the system cycles through the set of commands in the display file, drawing each component line in turn.
After all line-drawing commands have been processed, the system cycles back to the first line command in the list.
Random-scan displays are designed to draw all the component lines of a picture 30 to 60 times each second, with up to 100,000 “short” lines in the display list.