## Slide 1: PIC Instructions

## Slide 2: MOV - Data Transfer Instructions
MOVLW Immediate data - copy immediate data to WREG
MOVWF Destination – copy WREG to Destination
MOVF Register f, d
  Copy contents of Register f to a destination depending on d and a.
  If d=0, destination is WREG, else it is f.
  Status register (Z) gets affected

## Slide 3: ADD – Addition Instructions
ADDWF f,d – Contents of f and WREG are added
ADDWFC f,d – Contents of f, WREG and carry flag are added
  If d=0, destination is WREG else it is f.
ADDLW Immediate data – Immediate data is added to WREG
Status register is affected

## Slide 4: SUB – Subtraction instructions
SUBWF f,d  f – WREG
SUBFWB f,d  WREG(with Carry flag) – f
SUBWFB f,d  f(with Carry flag) - WREG
  If d=0, destination is WREG else it is f.
SUBLW Immediate data – Immediate data is subtracted from WREG
Status register is affected

## Slide 5
CLRF f,d
  Contents of register f are deleted and Z flag is set.
NEGF f,d
  Contents of register f are negated using two’s complement method.
  Status register is updated
COMF f,d
  Contents of register f are complemented using one’s complement method.
  Status register is updated
If d=0, result is stored in WREG, else it is in f.
Default value of d is 1.

## Slide 6: Access bank specifier
Opcode f,d,a
d and a are optional
If a=0, select the access bank
If a=1, bank is specified by BSR

## Slide 7
INCF f,d
  Increment file register f
INCFSZ f,d
  Increment file register f and skip the next instruction if f is zero
INCFSNZ f,d
  Increment file register f and skip the next instruction if f is not zero

## Slide 8
DECF f,d
  Decrement file register f
DECFSZ f,d
  Decrement file register f and skip the next instruction if f is zero
DECFSNZ f,d
  Decrement file register f and skip the next instruction if f is not zero

## Slide 9: Logic instructions
ANDLW Immediate data
ANDWF f,d
IORLW Immediate data
IORWF f,d
XORLW Immediate data
XORWF f,d

## Slide 10
CLRF f
  Contents of register f are deleted and Z flag is set.
NEGF f
  Contents of register f are negated using two’s complement method.
  Status register is updated
COMF f
  Contents of register f are complemented using one’s complement method.
  Status register is updated
Destination is f, as d is not mentioned , thus =1 (default)

## Slide 11
RLCF f,d
  Rotate left file register f, through carry flag
RLNCF f,d
  Rotate left file register f (not through carry flag)
RRCF f,d
  Rotate right file register f, through carry flag
RRNCF f,d
  Rotate right file register f (not through carry flag)

## Slide 12
Rotate left through carry(1)
Data = 58h
(01011000  1) (10110001 0)
10110000 - RLFNCF

## Slide 13
SWAPF f,d
  Swap nibbles in file register f.
  Ex. if f has data 35h
  After SWAPF instruction, data becomes 53h

## Slide 14: Bit b ranges from 0 to7
BCF f,b  clear bit b
BSF f,b  set bit b
BTG f,b  toggle (complement) bit b
10110010
BCF f,5  10010010
BSF f,0  10110011
BTG f,7 00110010

## Slide 16: Directives
ORG
END
EQU
SET
LIST  LIST target chip Ex. LIST PIC18F458
#include
radix  radix dec

## Slide 17
Assign value to a variable
A EQU 5
B SET 10
The value of A cannot be reassigned
The value of B can be reassigned

## Slide 18
X EQU a
a is hexadecimal by default
a can be in the format (hex)
  N, 0xN, NH, Nh, H’N’, h’N’
a can be in the format (decimal)
  D’N’, d’N’
a can be in the format (binary)
  B’N’, b’N’,
a can be in the format (ASCII)
  A’L’, a’L’, ‘L’

## Slide 19
  A EQU 41
  B EQU 0x41
  C EQU H’41’
  D EQU D’65’
  E EQU B’1000001’
  F EQU ‘A’
  G EQU A’A’

## Slide 20: GOTO Instruction
GOTO xyz
xyz:

## Slide 21: BNZ Instruction
Branch if not zero
 DECF
BNZ addr

## Slide 22
BZ – Branch if zero
BNC – Branch if no carry
BTFSC f,b  bit test skip next instruction if clear
BTFSS f,b  bit test skip next instruction if set

## Slide 23: Function call
CALL name-of-function
name-of-function
----
RETURN