## Slide 1: I/O port programming

## Slide 2: PIC18F458

## Slide 3
Block diagram of PIC18

## Slide 6: PORTS
PORTA, PORTB, PORTC, PORTD, PORTE
I/O, ADC, Timer, Interrupt, Serial communication pins

## Slide 7
PORTA – 7pins
PORTB,PORTC,PORTD – 8 pins
PORTE – 3 pins

## Slide 9
Each port is associated with 3 special function registers (SFR)
PORTx
TRISx (TRIState)
LATx (LATch)

## Slide 11: TRIS register
Make a pin in a port to input or output mode

## Slide 12: TRIS register
Make a pin in a port to input or output mode
0- output
1- input

## Slide 13: TRIS register
Make a pin in a port to input or output mode
0- output  data is copied to corresponding bit in PORTx register
1- input  data is read from corresponding bit in PORTx register

## Slide 14: Latch Registers
LATx registers are the port latch registers.

## Slide 15: Latch Registers
LATx registers are the port latch registers.
When a data is written to PORTx register, it is first stored in LATx register and then copied to PORTx.

## Slide 16: Latch Registers
LATx registers are the port latch registers.
When a data is written to PORTx register, it is first stored in LATx register and then copied to PORTx.
If TRISx register is not 0, then data is not copied to PORTx but remains in LATx.

## Slide 17: Latch Registers
When a data is read from PORTx register, it is first stored in LATx register and then copied to WREG.
If TRISx register is not 0xFF, then data is not copied from PORTx but from LATx.

## Slide 18: I/O ports and bit addressability

## Slide 19: I/O ports and bit addressability
BCF f,b  clear bit b
BSF f,b  set bit b
BTG f,b  toggle (complement) bit b

## Slide 20: I/O ports and bit addressability
BCF f,b  clear bit b
BSF f,b  set bit b
BTG f,b  toggle (complement) bit b
BTFSC f,b  bit test skip next instruction if clear
BTFSS f,b  bit test skip next instruction if set

## Slide 22
TRISB 01000001
PORTB=55H
LATB 01010101
PORTB 00010100 =14H

## Slide 23
PORTB 55H 01010101
AAH 10101010

## Slide 24: Read data from port B, add 5 to it and output sum at port C

## Slide 25: Read data from port B, add 5 to it and output sum at port C
MOVLW 0x00
MOVWF TRISC
MOVLW 0XFF
MOVWF TRISB
MOVF PORTB
ADDLW 0X5
MOVWF PORTC

## Slide 26: Read data from port C, add 5 to it and output sum at port B

## Slide 27: Read followed by a write operation

## Slide 28: Read followed by a write operation
Read data from Port C to WREG, store the data to Port B .

## Slide 29: Read followed by a write operation
Read data from Port C to WREG, store the data to Port B.
      CLRF TRISB
      SETF TRISC
      MOVF PORTC
      MOVWF PORTB

## Slide 30: Instruction flow or Pipelining
Instruction cycle consists of 4 cycles.
Fetch the instruction
Decode the instruction
Read the data
Execute the instruction

## Slide 31
Instruction 1 | Fetch | Decode | Read | Execute |  |  | 
Instruction 2 |  | Fetch | Decode | Read | Execute |  | 
Instruction 3 |  |  | Fetch | Decode | Read | Execute | 
Instruction 4 |  |  |  | Fetch | Decode | Read | Execute

## Slide 32
MOVF PORTC | Fetch | Decode | Read | Execute | 
MOVWF PORTB |  | Fetch | Decode | Read | Execute

## Slide 33
MOVF PORTC | Fetch | Decode | Read | Execute | 
MOVWF PORTB |  | Fetch | Decode | Read | Execute

## Slide 34
Data dependency
Read after write

## Slide 35
Read after read (No problem)
Read after write
Write after read
Write after write

## Slide 36: Read followed by a write operation
Read data from Port C to WREG, store the data to Port B.
      CLRF TRISB
      SETF TRISC
      MOVF PORTC
      NOP
      MOVWF PORTB

## Slide 37
MOVF PORTC | Fetch | Decode | Read | Execute |  | 
NOP |  | Fetch | Decode | Read | Execute | 
MOVWF PORTB |  |  | Fetch | Decode | Read | Execute

## Slide 38
      CLRF TRISB
      SETF TRISC
      MOVFF PORTC, PORTB

## Slide 39: Write a program to toggle the bits of ports B,C, and D every ¼ of a second. Assume the crystal frequency 4MHz.

## Slide 40
Crystal frequency : frequency of the crystal oscillator connected between OSC1 and OSC2 pins
The instruction execution time depends on this frequency

## Slide 42: Instruction cycle time for the PIC
The time taken for the CPU to execute an instruction is called instruction cycle or machine cycle.
All the instructions of PIC18 are either 2-byte or 4-byte
Most instructions take no more than 1 or 2 instruction cycles to execute.
In PIC18, one instruction cycle consists of 4 oscillator periods.
Therefore to calculate the instruction cycle for the PIC18, we take ¼ of the crystal frequency

## Slide 43
Data transfer instructions require 1 machine cycle except MOVFF (2 cycles)
Branch instructions require 2 machine cycles

## Slide 44: Delay calculations
Time delay = 0.25 s
Crystal frequency = 4 MHz
Instruction cycle frequency = 1MHz
Time of one cycle = 1 * 10-6 s
No operation instruction to be repeated for N cycles
  N= Time delay / time of one cycle = 0.25* 106 = 250000

## Slide 45
QDELAY
R1 EQU 0x05
R2 EQU 0x06
MOVLW n1
MOVWF R1
D1 MOVLW n2
MOVWF R2
D2 NOP
NOP
DECF R2
BNZ D2
DECF R1
BNZ D1
RETURN
For(r1=n1;r1>0;r1--)
{
for(r2=n2;r2>0;r2--)
{
nop
nop
}
}

## Slide 46
QDELAY
R1 EQU 0x05
R2 EQU 0x06
MOVLW n1
MOVWF R1
D1 MOVLW n2
MOVWF R2
D2 NOP
NOP
DECF R2
BNZ D2
DECF R1
BNZ D1
RETURN

## Slide 47
QDELAY
R1 EQU 0x05
R2 EQU 0x06
MOVLW n1
MOVWF R1
D1 MOVLW n2
MOVWF R2
D2 NOP
NOP
DECF R2
BNZ D2
DECF R1
BNZ D1
RETURN
N= n1*n2*5

## Slide 48
QDELAY
R1 EQU 0x05
R2 EQU 0x06
MOVLW n1
MOVWF R1
D1 MOVLW n2
MOVWF R2
D2 NOP
NOP
DECF R2
BNZ D2
DECF R1
BNZ D1
RETURN
N= n1*n2*5
N=250000
n1*n2=50000

## Slide 49
QDELAY
R1 EQU 0x05
R2 EQU 0x06
MOVLW n1
MOVWF R1
D1 MOVLW n2
MOVWF R2
D2 NOP
NOP
DECF R2
BNZ D2
DECF R1
BNZ D1
RETURN
N= n1*n2*5
N=250000
n1*n2=50000
n1=200
n2=250

## Slide 50
QDELAY
R1 EQU 0x05
R2 EQU 0x06
MOVLW D’200’
MOVWF R1
D1 MOVLW D’250’
MOVWF R2
D2 NOP
NOP
DECF R2
BNZ D2
DECF R1
BNZ D1
RETURN
N= n1*n2*5
N=250000
n1*n2=50000
n1=200
n2=250

## Slide 51
list P=PIC18F458
#include P18F458.INC
R1 EQU 0x07
R2 EQU 0x08
ORG 0
CLRF TRISB
CLRF TRISC
CLRF TRISD
MOVLW 0x55
MOVWF PORTB
MOVWF PORTC
MOVWF PORTD
LP COMF PORTB
COMF PORTC
COMF PORTD
CALL QDELAY
GOTO LP
QDELAY
MOVLW D’200’
MOVWF R1
D1 MOVLW D’250’
MOVWF R2
D2 NOP
NOP
DECF R2
BNZ D2
DECF R1
BNZ D1
RETURN
END

## Slide 52: Complement instruction
COMF reg , d
d= 0 or 1
Content of reg is complemented and stored in WREG if d is 0
Otherwise it is stored in reg.

## Slide 53: Complement instruction
COMF reg , d
d= 0 or 1
Content of reg is complemented and stored in WREG if d is 0
Otherwise it is stored in reg.
Instead of 0/1 we can use W/F.

## Slide 54
Branch instruction
BRA - equivalent to GOTO

## Slide 55
list P=PIC18F458
#include P18F458.INC
R1 EQU 0x07
R2 EQU 0x08
ORG 0
CLRF TRISB
CLRF TRISC
CLRF TRISD
MOVLW 0x55
MOVWF PORTB
MOVWF PORTC
MOVWF PORTD
LP COMF PORTB, F
COMF PORTC, F
COMF PORTD, F
CALL QDELAY
BRA LP
QDELAY
R1 EQU 0x05
R2 EQU 0x06
MOVLW D’200’
MOVWF R1
D1 MOVLW D’250’
MOVWF R2
D2 NOP
NOP
DECF R2
BNZ D2
DECF R1
BNZ D1
RETURN
END

## Slide 56: An LED is connected to each pin of Port D. Write a program to turn on each LED from pin D0 to pin D7. Call a delay module turning on next LED

## Slide 57
CLRF TRISD
BSF PORTD,0
CALL DELAY
BSF PORTD,1
CALL DELAY
BSF PORTD,2
CALL DELAY
BSF PORTD,3
CALL DELAY
BSF PORTD,4
CALL DELAY
BSF PORTD,5
CALL DELAY
BSF PORTD,6
CALL DELAY
BSF PORTD,7
CALL DELAY