## Slide 1: Prescaler and generating a large time delay

## Slide 2
The time delay(t) depends on crystal frequency (f) and value in timer’s 16 bit register(r).
The time delay is inversely proportional to both crystal frequency and the value in timer’s 16 bit register.
i.e. t ∝ 1/f and t ∝ 1/r

## Slide 3
We have seen that the maximum delay generated for the crystal frequency 10 MHz without prescaler is 26.2144 ms.
If we want to generate more delay, then we should use prescaler

## Slide 5
Find the timer’s clock frequency and its period for PIC18, with crystal frequency 16 MHz. Assume that a prescaler of 1:64 is used.
Crystal frequency = 16 MHz
Microcontroller frequency = 16/4 = 4 MHz.
Frequency due to prescaler = 4/64 = 0.0625 MHz= 62500 Hz.
Timer’s period = 1/62500 = 16 µs

## Slide 6
Find the delay (in seconds) generated by the following program. Exclude the overhead due to the instructions in the loop. Assume XTAL = 10 MHz

## Slide 8
T0CON = 0x05

## Slide 9
T0CON = 0x05
0 0 0 0 0 1 0 1
Counter 16 bit transition increment Prescaler 1:64 prescale
timer off on cycle on +ve assigned
clock edge

## Slide 10
T0CON = 0x05
0 0 0 0 0 1 0 1
Counter 16 bit transition increment Prescaler 1:64 prescale
timer off on cycle on +ve assigned
clock edge
Timer frequency = 10/4/64 = 390625 Hz
Timer cycle = 1/390625 = 25.6 µs
Count = FFFFH – 0108H+1 = FEF8H = 65272
Time delay = 65272 * 25.6 µs = 1.671 s

## Slide 11
What is the maximum time delay that can be generated using timer 0, with prescaler. Assume XTAL = 10 MHz.

## Slide 12
What is the maximum time delay that can be generated using timer 0, with prescaler. Assume XTAL = 10 MHz.
Timer frequency = 10/4/256 = 9765.625 Hz
Time cycle = 1/9765.625 = 102.4 µs
Count = FFFFH – 0000H+1 = 10000H = 65536
Time delay = 65536 * 102.4 µs = 6.710886 s

## Slide 13
Write a program to generate a square wave of 50 Hz frequency on pin PORTB.7. Use Timer0, 16-bit mode, with prescaler = 128

## Slide 14
Counter 16 bit transition increment Prescaler
timer off on cycle clock on +ve edge not assigned
low to high
0 0 0 0 0 1 1 0

## Slide 15
Counter 16 bit transition increment Prescaler
timer off on cycle clock on +ve edge not assigned
low to high
0 0 0 0 0 1 1 0
T0CON = 06H

## Slide 16
Given :
Frequency of square wave = 50 Hz.
Full cycle delay = 1/50 = 0.02 s = 20 ms.
Half cycle delay = 10 ms.
t= 10 ms = 10000 µs
f= 10 MHz

## Slide 17
n = t*f /4/128 = 10000*10/4/128 = 195.3125 = 195
c= 65536 – n = 65536 – 195 = 65341
Convert c to Hex = FF3DH
Set TMR0H = FFH and TMR0L = 3DH

## Slide 18
BCF TRISB, 7
MOVLW 0x06
MOVWF T0CON
L1 MOVLW 0xFF
MOVWF TMR0H
MOVLW 0x3D
MOVWF TMR0L
BCF INTCON, TMR0IF
BTG PORTB, 7
BSF T0CON, TMR0ON
L2 BTFSS INTCON, TMR0IF
BRA L2
BCF T0CON, TMR0ON
BRA L1

## Slide 19: 8 bit Timer programming
TMR0L – 00H to FFH
Start the timer0
  Set the timer on bit
  BSF T0CON, TMR0ON or BSF T0CON,7
It starts to count up till FFH then back to 00H.
  When it reaches FFH, timer interrupt flag (TMR0IF ) of interrupt control register (INTCON) is set.
In order to repeat the process, load the TMR0L registers with the original value and reset TMR0IF.

## Slide 20
Timer frequency = f = crystal frequency/4 (/ prescale if applicable)
Each clock period = t = 1/f
Time delay= number of counts * clock period
Number of counts = c = FFH – (value in TMR0L) +1(rolling back) (in decimal)
Time delay(half cycle) = c * t
Time delay(full cycle) = 2 * c * t

## Slide 21: Assuming that XTAL = 10 MHz, find the frequency of the square wave generated on pin PORTB.0 in the following program

## Slide 22: Assuming that XTAL = 10 MHz, find the frequency of the square wave generated on pin PORTB.0 in the following program
Timer frequency = f = 10/4 = 2.5 MHz

## Slide 23: Assuming that XTAL = 10 MHz, find the frequency of the square wave generated on pin PORTB.0 in the following program
Timer frequency = f = 10/4 = 2.5 MHz
Each clock period = t = 1/f = 1/2.5 = 0.4 µs

## Slide 24: Assuming that XTAL = 10 MHz, find the frequency of the square wave generated on pin PORTB.0 in the following program
Timer frequency = f = 10/4 = 2.5 MHz
Each clock period = t = 1/f = 1/2.5 = 0.4 µs
Time delay= number of counts * clock period

## Slide 25: Assuming that XTAL = 10 MHz, find the frequency of the square wave generated on pin PORTB.0 in the following program
Timer frequency = f = 10/4 = 2.5 MHz
Each clock period = t = 1/f = 1/2.5 = 0.4 µs
Time delay= number of counts * clock period
Number of counts = c = FFH – 5 +1 = FBH = 251

## Slide 26: Assuming that XTAL = 10 MHz, find the frequency of the square wave generated on pin PORTB.0 in the following program
Timer frequency = f = 10/4 = 2.5 MHz
Each clock period = t = 1/f = 1/2.5 = 0.4 µs
Time delay= number of counts * clock period
Number of counts = c = FFH – 5 +1 = FBH = 251
Time delay(half cycle) = 251*0.4 = 100.4 µs

## Slide 27: Assuming that XTAL = 10 MHz, find the frequency of the square wave generated on pin PORTB.0 in the following program
Timer frequency = f = 10/4 = 2.5 MHz
Each clock period = t = 1/f = 1/2.5 = 0.4 µs
Time delay= number of counts * clock period
Number of counts = c = FFH – 5 +1 = FBH = 251
Time delay(half cycle) = 251*0.4 = 100.4 µs
Time delay(full cycle) = 200.8 µs

## Slide 28: Assuming that XTAL = 10 MHz, find the frequency of the square wave generated on pin PORTB.0 in the following program
Timer frequency = f = 10/4 = 2.5 MHz
Each clock period = t = 1/f = 1/2.5 = 0.4 µs
Time delay= number of counts * clock period
Number of counts = c = FFH – 5 +1 = FBH = 251
Time delay(half cycle) = 251*0.4 = 100.4 µs
Time delay(full cycle) = 200.8 µs
Frequency of square wave = 1/200.8 = 4980.78 Hz = 4.980 KHz

## Slide 29: What is the possible minimum frequency of the square wave generated using 8 bit timer0 and prescaler 256.

## Slide 30: What is the possible minimum frequency of the square wave generated using 8 bit timer0 and prescaler 256. Assume XTAL = 10 MHz
Timer frequency = f = 10/4 = 2.5 MHz
Each clock period = t = 1/f/prescaler = 1/2.5/256 = 1.5625 ms
Time delay= number of counts * clock period
Number of counts = c = FFH – 0 +1 = 100H = 256
Time delay(half cycle) = 256*1.5625 = 400 ms
Time delay(full cycle) = 800 ms
Frequency of square wave = 1/800 = 1.25 Hz